## Slide 1
17.2 Current
pages 593-599
Let’s get an introduction!

## Slide 2: Voltage & Batteries
Voltage (potential difference) across two ends (terminals) of a battery ranges from 1.5 V (small battery) – 12 V (car)
  Voltage causes charges to move
  Batteries are cells: devices that produce an electric current by converting chemical energy into electrical energy
  contains:
    electrolytes: electrically conducting solution
    electrodes: two; each different
    conductive material
    can be dry or wet
As voltage increases,
current increases (and vice versa)
This is a direct relationship.

## Slide 3: Electric Current
Electric current: rate at which charges (e-) move through a conductor
  Current is measured in amperes (A)
Direction of current is opposite to the direction the e- move
  WHY?!

## Slide 4: Current & E- Flow Opposite
+ -
Electrons will flow towards the opposite charge. That’s which direction? Right to left
  electrons
But current is the opposite direction. Left to right.
  current
So current does flow from positive to negative.
And electrons do get pulled towards the positive charge (negative to positive)
But we define electric current to be the opposite direction of electron flow.

## Slide 5: Electrical Resistance
Light bulbs use different amounts of power b/c different currents in them
  Difference in currents is due to resistance
Resistance: caused by internal friction  slows the movement of charges
through a conductor
Resistance = voltage
  current
R = V
I
R= resistance (ohm Ω)
V= voltage (volts V)
I= current (amperes A)
LET’S TRY SOME EXAMPLES ON YOUR NOTEGUIDE!

## Slide 6: Conductors vs. Insulators
Conductors have low resistance
  Electrons flow easily
Insulators have high resistance
  Electrons do not flow easily
Semiconductors conduct under certain conditions
  Pure state: insulators
  Addition of specific atoms allows electric charge to be conducted (conductor)
  Used in manufacturing of most electronic devices
    Necessary due to change in temp & composition  can alter conductivity
    Ex: Silicon and Germanium in computer boards

## Slide 7: Alternating vs. Direct Current
Alternating Current (AC):
  Power that comes from a power plant
  Direction of current switches or alternates (60 times per second!)
  The power we receive from a wall socket in the U.S. is 120V, 60 cycle alternating power.

## Slide 8: Alternating vs. Direct Current
Direct Current (DC):
  Batteries, fuel cells, and most electronic devices all produce DC.
  The + and – terminals of a battery are always respectively positive and negative.
    Current is always in the one direction (direct) between two terminals.

## Slide 9: So why have two types of current?
Ben Franklin AC vs. DC video clip
The reason we have two types of current is because AC is best used for power grids.
  AC able to travel far distances efficiently
However, DC is commonly used in household appliances, etc.
  Because these devices need DC, that means that the device has to convert AC to DC and sometimes energy is lost in the form of HEAT (which is why your laptop may feel warm).

## Slide 10: 17.3 Circuits: Series/Parallel p. 603
Circuit: set of electrical components connected such that they provide one or more complete paths for the movement of charges
Circuits can be:
  Open
  Closed

## Slide 11
Series
Single path for current
Amount of charge that enters a device = amount of charge that exits a device
Current in each device is same, resistances may be different depending on the device (light bulb etc.)
  Voltage across each device may be different
One element in circuit removed, charges would not move
  circuit is open
Parallel
Multiple paths for current
Amount of charge that enters may be different from the amount that exits
Current in each device does not have to be the same  sum of currents in all devices = total current
  Voltage across each device is the same
One element in circuit is removed, charges would still move through other loop(s)